ReefBerry Pi API Reference Guide

# Remote Procedure Calls (RPC)

## get_probedata24h[probetype, probeid]

Request:
probetype	probeid
ds18b20	28-xxxxxxxxxxxx	for ds18b20 temperature probes, probeid is the id code associated with the ds18b20 temperature probe / (ex: 28-0416525c5fff)
mcp3008	0 / 1 / 2 / 3 / 4 / 5 / 6 / 7	For mcp3008 a/d converter. Probeid is any number from 0-7 to specify which of the 8 channels to retrieve data on
dht	t / h	For DHT11 or DHT22 temperature and humidy sensor. Probeid t to retrieve temperature data, or h for humidity

Return:
data
	datetime	Formatted as 24 hour time in format as: / YYYY-mm-dd HH:MM:SS
	probevalue	Will receive data as either C or F depending on server preference in single decimal format: / xx.x

JSON Example:

request object:
{
    “rpc”: “get_probedata24h”,
    “probetype”: “ds18b20”,
    “probeid”: ”28-0416525c5fff”
}

return object:
{
    “datetime”: [“2018-12-30 01:07:48” , … , “2018-12-31 13:09:20],
    “probevalue”: [“78.1”, … , “77.5”]
}
rpc_get_outletstate[bus, outletnum]

bus	outletnum
int	1 / 2 / 3 / 4 / 5 / 6 / 7 / 8	Relays connected directly to pins on Raspberry Pi
ext	1 / 2 / 3 / 4 / 5 / 6 / 7 / 8	Relays connected to pins on Arduino and controlled by Raspberry Pi via USB connection

JSON Example:

request object:
{
    “rpc”: “rpc_get_outletstate”,
    “bus”: “int”,
    “outletnum”: ”1”
}

return object:
{
    “outletstate”: “on”
}

rpc_set_outletstate[bus, outletnum, value]

bus	int / ext	int: Relays connected directly to pins on Raspberry Pi / ext: Relays connected to pins on Arduino and controlled by Raspberry Pi via USB connection
outletnum	1 / 2 / 3 / 4 / 5 / 6 / 7 / 8	Each bus supports up to 8 outlets.
value	on / off	Turn outlet on or off

JSON Example:

request object:
{
    “rpc”: “rpc_set_outletstate”,
    “bus”: “int”,
    “outletnum”: ”1”
    “value”: “off”
}

return object:
{
    “outletstate”: “off”
}

# Broadcast Updates

## status_currentprobeval

JSON Example:

broadcast object:
{
    “broadcast”: “status_currentprobeval”,
    “probetype”: “ds18b20”,
    “probeid”: ”28-0416525c5fff”
    “probeval”: “77.8”
}

## status_currentoutletstate

JSON Example:

broadcast object:
{
    “broadcast”: “status_currentoutletstate”,
    “bus”: “int”,
    “outletnum”: ”1”
    “state”: “off”
    “mode”: ”auto”
    “status”: “OFF (77-78)”
}